## Slide 1: CS 736: Advanced Operating Systems Andrea Arpaci-Dusseau Lecture 2: Background – Disks and File Systems
3 Papers for Today: Disk Modeling and FFS and A File is Not a File
Cannot talk about everything or even everything that is interesting!
Questions for Today:
How do the physical characteristics of disks impact I/O performance?
What techniques did FFS use to improve performance?
How have file system workloads changed since FFS?
Meta-goal for Today: Get everyone to speak in first two “real” classes
To do for Tuesday:
Read papers and answer question for next lecture: RAID and LFS
Plan for first reading group
Notes: Goal: Get everyone to speak to class in first two lectures; don’t want long-winded opinions in this course, but do want people to talk and show they are involved and what they understand
Do I have about 50 straight-forward questions in here?
Questions in this lecture today and rather straight-forward and don’t even correspond exactly to reading, so don’t have to feel bad if you do or don’t know answers. Try to not answer multiple times if other people in your row haven’t answered!
I’m not going to track who talks today, this is really for your benefit so you feel comfortable.

## Slide 2: Paper #1
Chris Ruemmler and John Wilkes An introduction to disk drive modeling IEEE Computer 27(3):17–29, March 1994.
Why this paper?
  Understand technology that still influences current system software
    What should change and what should stay the same?
    How much knowledge should one layer use of layer beneath?
  Useful to model or simulate other layers
    Mini-project: Simulation of SSD
    How accurate vs. complex does model need to be?

## Slide 3: What is in a Hard Disk Drive (HDD)?
Electromechanical
  Rotating disks
  Arm assembly
Electronics
  Disk controller
  Cache
  Interface controller

## Slide 4: Disk Terminology
spindle
platter
surface
track
cylinder
sector (512 bytes)
read/write head
Blocks: Group of consecutive sectors
Sector also has overhead information
  Error Correcting Codes (ECC)
  Servo fields to properly position the head
1?
2?
3?
4?
5?
6?
7?
Notes: Amazing engineering: read spins above surface at height much less than thickness of human hair
Sectors are tiny…hard to figure out exactly which sector head is above at any instant in time
Deal with these platters wobbling slightly
Typical size? 80 GB disks
ZBR (Zoned bit recording): More sectors on outer tracks

## Slide 5: HDD Organization
Typical configurations seen in hard disks
  Platter diameters: 3.7”, 3.3”, 2.6”; Mobile disks can be as small as 0.75”
  RPMs: 5400, 7200, 10000, 15000
    0.5-1% variation in the RPM during operation
  Number of platters: 1-5
Hypothetical disk:
  # surfaces: 4
  # tracks/surface: 16K
  # sectors/track: 256
  # bytes/sector: 512 bytes
What is the capacity?
  4*16K*256*512 = 8GB
Energy consumption is important issue
How can you change disk to reduce power (with same capacity)?
Power proportional to: (# Platters)*(RPM)2.8(Diameter)4.6
  Tradeoff in the drive-design

## Slide 6: Density is increasing!
Density determines capacity and performance
How is density measured?
  Linear density (Bits/inch or BPI)
  Track density (Tracks/inch or TPI)
  Areal Density = BPIxTPI
BPI
TPI

## Slide 7: How to Increase Density?
Magnetic domains oriented in the direction in which head travels
Soft underlayer (mirrors) write field and allows domains to be closer
Longitudinal Recording
Perpendicular Recording

## Slide 8: Increase Capacity with Shingled Disks
Observation: Writes are wider than reads and require gap to not interfere
SMR: Shingled Magnetic Recording – Increase density further
Allow writes to overlap one another
Must write to larger group
Can still read smaller amount
Change interface  Change local file systems too?

## Slide 9: Disk Performance
How long to read or write n sectors?
  Positioning time + Transfer time (n)
  Question: What is positioning time?
    Positioning time: Seek time + Rotational Delay
    Seek: Time to position head over destination cylinder
    Rotation: Wait for sector to rotate underneath head
  What is transfer time?
    Transfer time: n / (RPM * bytes/track)
Typical access time?
  Order of milliseconds (RAM? Nanoseconds!)
Notes: Accessing a disk takes order of milliseconds

## Slide 10: How long to seek?
Components of a seek:
  Speedup
    Arm accelerates
  Coast
    Arm moving at maximum velocity (long seeks)
  Slowdown
    Arm brought to rest near desired track
  Settle
    Head is adjusted to access desired location
Very short seeks (2-4 cylinders)
  Dominates?
Short seeks (200-400 cylinders)
  Dominates?
Longer seeks
  Dominates?
With smaller platter-sizes and higher TPI?
  Settle-time becoming more important
Simple seek model – Linear in distance
Settle-time
Speedup/Slowdown-time
Coast-time

## Slide 11: Switching Time
Head Switch: Switch data channel from one surface to next in same cylinder
  Vertical alignment of cylinders difficult at high TPI
  Head might need to be repositioned during the switch
  Can be 1/3-1/2 of settle-time
Track Switch: Position moves from last track of cylinder to first track of next cylinder
  Almost same amount as the settle-time
At high TPI, head-switching and track-switching times are nearly the same

## Slide 12: How to Optimize Settle Time?
1) Optimistic Positioning
  Attempt read when head is near the desired track
  ECC and sector ID determine if correct data was read
  Not done for settle before write!
2) Track Skewing
  Provides faster sequential access across track and cylinder boundaries
  Skew logical sector zero of each track by worst-case head/track switch-time
  Each zone has different skew factors

## Slide 13: Data Layout
Logical blocks mapped to physical sectors on disk drive
Low-Level Layout Factors
  Track Skewing
  Sparing
  Serpentine Layout
D
A
A
A
B
B
B
B
C
C
C
B
B
D
D
D
D
B
Logical view of disk by OS: Linear array (list) of blocks
  Zoned-Bit Recording (ZBR or multi-zone disk)
    Outer tracks can hold more sectors due to larger perimeter
    Outer zones experience higher data rates.
    Modern disks have about 30 zones

## Slide 14: Zoned-Bit Recording
Outer tracks can hold more sectors due to larger perimeter
Per-track storage-allocation requires complex channel electronics
Tradeoff:
  Group tracks in zones
  Outer zones allocated more sectors than inner ones
  Due to constant angular velocity, outer zones experience higher data rates.
Modern disks have about 30 zones

## Slide 15: On-Disk Cache
Track buffer or larger segmented disk cache
  Typically 8-16 MB for modern disks
Reads
  Sequential reads: Actively reading disk data and placing in cache
Writes
  What are 3 advantages of buffering writes in disk cache?
    Time for write to cache is much faster than disk surface
    Provides write-coalescing for better utilization of disk bandwidth
    Many write requests enables disk scheduling opportunities
  What is the disadvantage?
    Reliability: What if power failure before write to surface?
    Immediate Reporting: Writes are done as soon as they are written to cache
    Disable Immediate Reporting if care about durability!
Will revisit this for crash consistency in OptFS…

## Slide 16: Tagged Command Queuing
Disk can schedule multiple requests itself
  Disks know low-level layout for best ordering
Names of disk scheduling algorithms?
SCAN and elevator
  Handle requests in order by cylinder
  Variation: C-SCAN: Start requests in same dir always
Shortest-seek-time-first (SSTF)
Shortest-positioning-time first (SPTF)
  Take rotational delay into account as well

## Slide 17: Drive Electronics
ECC
  Appends ECC symbols, performs error-handling operations
  Current disks employ Reed-Solomon codes
Servo Control
  For necessary signal-processing for disk-rotation and head positioning
  Needed due to motor variation, platter waviness (circumferentially and radially), stacking tolerances, vibrations, etc.

## Slide 18: Reliability
Key metric – Mean-Time Between Failures (MTBF)
Typical MTBF for SCSI disk = 1,200,000 hours
  Typically the first-year reliability
  Assumes “nominal” operating conditions
Environmental Factors Affecting Reliability?
Temperature
  Reliability decreases with increase in temperature
  15 C rise in room temp can double failure-rate
Vibrations
  Caused by moving components nearby
  Cause off-track errors that delay I//O or cause temporary errors
  Worse at high TPI due to smaller tolerances
  Server-disks designed for more vibration tolerance
Will revisit reliability when we discuss RAID

## Slide 19: Disk in Action

## Slide 20: Paper #2
McKusick, M.K., Joy, W.N., Leffler, S.J., and Fabry, R.S. A Fast file System for UNIX ACM Transactions on Computer Systems (TOCS) Vol. 2, No. 3, August 1984, pp. 181-197.
Why this paper?
  Meta-reasons
    Hall of Fame paper: Recognized by systems community as influential
    Good starter paper (already familiar with concepts)
  Technology contributions
    Good background for basic file system design
    Good example of system designed for underlying technology and workload
    Good example of measurement / implementation feedback loop

## Slide 21: FFS Motivation
Original UNIX file system from Bell Labs
  Simple and elegant
  Problem: Achieves 20 Kb/sec
    2% of disk maximum even for sequential disk transfers!
Why such poor performance?
  Three high-level reasons…
  Focus first on problems (not solutions)
Data Blocks
super block
inodes

## Slide 22: Why such poor performance?
3) No locality in allocation to disk; Two problems?
  I-nodes far from data blocks
    Pay two seeks for every data transfer
  I-nodes of files in directory not close together
    Pay seek for every i-node (e.g., ls -l)
1) Blocks too small (512 bytes); Two problems?
  Fixed costs per transfer
    Seek time, rotational delay, computation
  More indirect blocks needed for same size ﬁle
2) Poor freelist organization; Problem?
  Consecutive file blocks not close together
    Pay seek cost between even sequential disk transfers

## Slide 23: #1: Larger Block Sizes
Measure FS performance given different block sizes
Increase from 512 bytes to 1KB doubled performance
BSD: Why not increase block to 4096 or 8192 bytes?
What is the problem with larger blocks?
Most file are very small, even today!

## Slide 24: Solution to Internal Fragmentation?
Fragments: Chop up large blocks into 2, 4, or 8 pieces
  Lower bound on fragment size determined disk sector
  Keep track of free fragments
Beneficial for small files and ends of files
Algorithm for ensuring fragments only used for end of file
  Only allocate fragments from one block per file
  Coallesce blocks of allocated fragments

## Slide 25
AAAA
File A, size 5KB
File B, size 2KB
B
A
B

## Slide 26
AAAA
File A, size 6KB
File B, size 2KB
B
A
B
A
append A to first file

## Slide 27
AAAA
File A, size 7KB
File B, size 2KB
B
A
B
A
append A to first file
Not allowed to use fragments across multiple blocks!
What to do instead?
A

## Slide 28
AAAA
AAAA
File A, size 8KB
File B, size 2KB
B
B
append A to first file, copy to fragments to new block

## Slide 29: Fragments: Pros and Cons
Performance problem if file grows a fragment at a time
  New API to write to block-sized chunks
Advantages: Best of small and large blocks
  Small: Greatly reduces amount of wasted space
  Large: Transfer speeds of larger blocks

## Slide 30: #2: Unorganized Freelist
Leads to random allocation of sequential files over time
Initial performance good
...but FS are long-lived entities
What are 3 possible solutions?

## Slide 31: Fixing the Unorganized Freelist
Periodically compact / defragment disk
  Disadvantage: Disk not accessible during operation
Organize freelist by address; Disadvantages?
  Costly to insert
  Non-trivial to find N contiguous free blocks
Bitmap of free blocks
  Solution used in BSD
  Bitmap: 100100001101101011111
Data Blocks
super block
inodes
bitmaps

## Slide 32: #3: Locality
Techniques for keeping related items together
Spread unrelated data far apart
  Leaves room for related things to be placed together
Requirement: freespace on disk
  Always find free block near desired location
  Rule of thumb: do not exceed 90% utilization
What new organization structure to support locality did BSD introduce?

## Slide 33: New organization structure?
Divide disk into cylinder groups
  Set of adjacent cylinders
  Little seek time between cylinders in same group
Each cylinder groups contains?
  Superblock
    Vary offset within each cylinder group for reliability
  I-nodes
    Fixed number per cylinder group
  Bitmap of free blocks
  Usage summary for high-level allocation policy
  Data blocks
D
S
I
B
D
S
I
B
D
S
I
B
…

## Slide 34: Goals for Locality
Maintain locality of each ﬁle
Maintain locality of ﬁles and inodes in a directory
Make room for locality within a directory
How does BSD achieve each of these goals?
  What heuristics does it use when allocating blocks to disk?

## Slide 35: Solution to Achieving Locality
Maintain locality of each file
  Allocate runs of blocks within a cylinder group
Maintain locality of files and inodes in a directory
  Keep files in a directory in same cylinder group
Make room for locality within a directory
  Spread out directories among the cylinders groups
    Greater than average # of free inodes, smallest # of directories
  Switch to a different cylinder group for large ﬁles
    After 48KB and every 1MB thereafter
    Prevent one ﬁle from ﬁlling a cylinder group
    Greater than average # of free data blocks

## Slide 36
dir data
file inode
dir inode
B1
B2
B3
B1
B2
Where to cut the tree and start
growing into another group?
pointer
related
many
break
Ind
B3
B4
break
dir inode

## Slide 37: Layout: Global vs. Local
Decompose allocation into two steps
Global: Heuristics for allocating files+directories to cylinder groups
Pick “optimal” next block for allocation
Local: Handles request for specific block
  If block available, use it
  If not free, check a sequence of alternatives
    Next rotational block on same cylinder
    A block within cylinder group
    Rehash on cylinder group to choose another group
    Exhaustive search

## Slide 38: Rotationally Optimal Placement
Skip-sector allocation
  Based on CPU and device speed
  Do not allocate contiguous sectors if CPU not fast enough
Problems?
  Cannot achieve full bandwidth from disk
  Timing may be optimal for reads but not writes
  Best allocation changes if move disk between machines
No longer an issue in current systems!

## Slide 39: BSD Performance Improvements
Achieve 20-40% of disk bandwidth on large files
  10x improvement over original Unix file system
  Does not change over lifetime of FS
  Especially good considering skip-sector allocation
    Could not achieve better than 50% of peak
Better small file performance than previously

## Slide 40: Conclusions
General
  Know performance/reliability of underlying components
  Measure your system to improve it!
FFS
  Fragments: Useful when storage capacity is limited
  Cylinder groups: Structure to aid locality and improve perf
  Locality: Keep inodes and data blocks from same file + dir together

## Slide 41: A file is Not a file: Understanding the I/O Behavior of Apple Desktop Applications
Tyler Harter, Chris Dragga, Michael Vaughn,
Andrea C. Arpaci-Dusseau, Remzi H. Arpaci-Dusseau
Department of Computer Sciences
University of Wisconsin-Madison
SOSP '11 Proceedings of the ACM Symposium on Operating Systems Principles

## Slide 42: Why this paper?
Meta-issues
  Best Paper from SOSP’11
  Paper from UW-Madison
  Exposure to modern paper style
Technical Contributions
  Many thorough measurements about current desktop workloads
  Low-level data plus high-level summary observations
  Incentive to think about implications for future file systems

## Slide 43: Why study desktop applications?
Measurement drives file-system design
  file systems must decide how to optimize
Great history - many past I/O studies
  SOSP ’81: M. Satyanarayanan. A Study of file Sizes and Functional Lifetimes.
    Influenced AFS and Code (read later)
  SOSP ’85:, Ousterhout et al. A Trace-Driven Analysis of Name and Attribute Caching in a Distributed System.
  SOSP ’91: M. Baker et al. Measurements of a Distributed System.
  SOSP ’99: W. Vogels. file system usage in Windows NT 4.0.
There is still uncharted territory
  Little focus on home users
  Little focus on individual applications
  More study can inform the design of the next generation of file systems

## Slide 44: A case study: saving a document
Application: Pages 4.0.3
  From Apple’s iWork suite
  Document processor (like MS Word)
One simple task (from user’s perspective):
  Create a new document
  Insert 15 JPEG images (each ~2.5MB)
  Save to the Microsoft DOC format

## Slide 45: iBench Task Suite
  iLife suite (multimedia)
    iPhoto 8.1.1
    iTunes 9.0.3
    iMovie 8.0.5
  iWork (like MS Office)
    Pages 4.0.3 (Word)
    Numbers 2.0.3 (Excel)
    Keynote 5.0.3 (PowerPoint)
Automate 34 typical tasks: Importing photos, playing songs, editing movies,
  typing documents, making charts, displaying a slideshow
Collect I/O traces : Use DTrace to instrument kernel
  System-call level traces reveal application behavior
  Record I/O events: open, close, read, write, fsync, etc.

## Slide 46
files
small I/O
big I/O

## Slide 47: Case study observations
Auxiliary files dominate
  Task’s purpose: create 1 file; observed I/O: 385 files are touched
  218 KV store files + 2 SQLite files:
    Personalized behavior (recently used lists, settings, etc)
  118 multimedia files:
    Rich graphical experience
  25 Strings files:
    Language localization
  17 Other files:
    Auto-save file and others

## Slide 48
Files opened

## Slide 49: General observations
Auxiliary files dominate
  Lots of helper files
  With hundreds of helper files, how can we minimize disk seeks?

## Slide 50
Threads
files
small I/O
big I/O

## Slide 51: Case study observations
Auxiliary files dominate
Multiple threads perform I/O
  Interactive programs must avoid blocking

## Slide 52
fsync
files
Threads
small I/O
big I/O

## Slide 53: Case study observations
Auxiliary files dominate
Multiple threads perform I/O
Writes are often forced
  KV-store + SQLite durability
  Auto-save file

## Slide 54
Write I/O bytes

## Slide 55: General observations
Writes are often forced
  Renders write buffering ineffective
  Can hardware help?
  What do applications need? Durability? Ordering?

## Slide 56
rename
files
Threads
fsync
small I/O
big I/O

## Slide 57: Case study observations
Auxiliary files dominate
Multiple threads perform I/O
Writes are often forced
Renaming is popular
  Often used for key-value store
  Makes updates atomic

## Slide 58
Locality
Implications
Write I/O bytes

## Slide 59: General observations
Renaming is popular
  How should directory-locality heuristics adapt?
  Do we need atomicity APIs?

## Slide 60
files
Threads
rename
fsync
small I/O
big I/O

## Slide 61
read
write
Writing the
DOC file

## Slide 62: Case study observations
Auxiliary files dominate
Multiple threads perform I/O
Writes are often forced
Renaming is popular
A file is not a file
  DOC format is modeled after a FAT file system
    Multiple “sub-files”
    Application manages space allocation

## Slide 63
Mostly Complex
files
files, (weighted by I/O)

## Slide 64: General observations
A file is not a file
  Complex files have a significant presence
  Should file system be aware of structure within a file?
  How can file system allocate space for sub files in complex files?

## Slide 65
read
write
Writing the
DOC file

## Slide 66: Case study observations
Auxiliary files dominate
Multiple threads perform I/O
Writes are often forced
Renaming is popular
A file is not a file
Sequential access is not sequential
  Multiple sequential runs in a complex file => random accesses

## Slide 67
Prefetching
Implications
Read I/O bytes

## Slide 68: General observations
Auxiliary files dominate
A file is not a file
Sequential access is not sequential
  How can we prefetch intelligently based on patterns?

## Slide 69
read
write
Writing the
DOC file

## Slide 71: Case study observations
Auxiliary files dominate
Multiple threads perform I/O
Writes are often forced
Renaming is popular
A file is not a file
Sequential access is not sequential
Frameworks influence I/O
  Example: update value in page function
  Cocoa, Carbon are a substantial part of application

## Slide 72: Conclusion: how has the world changed?
In the past, applications:
  Used the file-system API directly
  Performed simple tasks well
  Chained together for more complex actions
Today, we see:
  Applications are graphically rich, multifunctional monoliths
  “#include <Cocoa/Cocoa.h> reads 112,047 lines from 689 files” ~ Rob Pike ‘10
  They rely heavily on I/O libraries
Cocoa, Carbon,
and other frameworks
file System
Developer’s Code
file System
Application

## Slide 73: CS 736: Advanced Operating Systems Andrea Arpaci-Dusseau Lecture 2: Background – Disks and File Systems
3 Papers for Today: Disk Modeling and FFS and A File is Not a File
Cannot talk about everything or even everything that is interesting!
Questions for Today:
How do the physical characteristics of disks impact I/O performance?
What techniques did FFS use to improve performance?
How have file system workloads changed since FFS?
Meta-goal for Today: Get everyone to speak in first two “real” classes
To do for Tuesday:
Read papers and answer question for next lecture: RAID and LFS
Plan for first reading group